NetPractice:

Discover Networking.
Understand how TCP/IP addressing works.
Complete 10 levels.
Solve networking problems to make a network run
Basic understanding what you will do:

1)	You will have to configure small-scale networks.

2)	To do so, it will be necessary to understand how TCP/IP addressing works.
IP addressing is a logical means of assigning addresses to devices on a network.
Each device connected to the internet requires a unique IP address.

Identify the device and the network it is connected to.

3)	0nly IPv4 addresses are used in NetPractice.

4)	Private IP addresses and subnetting are features provided by routers,
which create a local network (LAN) and use Network Address Translation (NAT)
to share a single public IP address among multiple devices within that network.

Therefore, for devices to have private IP addresses and to form a private network,
they need to be connected to a router.

Network fundamentals:

1.	IP	Internet Protocol address. / - Network ID / - Host ID
	Types of IP address	Static IP address: / - doesn’t change / - business, servers / Dynamic IP address: / - changes occasionally / - consumer equipment, laptop, smartphones, tablet
	Purpose of the IP address	- handle connection beween devices / - let the websites know who is connecting
	IPv4 v IPv6	IPv4 / - 32 bits address / 4 octets / - 4.3 billion addres, insufficient / - must be reused and masked / - 192.108.42.64 / IPv6 / - 128 bits address / - trillions and trillions / - every device can have unique IP / - supports auto-configuration
	TCP / IP	Transmission Control Protocol/Internet Protocol / Governs rules for / - Packetizing / - Addressing / - Transmitting / - Routing / - Receiving data over networks
	TCP v IP	Seperate computer network protocols / IP – obtains the address / TCP – responsible for data delivery to the address
	TCP/IP work	4 layers / - Datalink – physical part, Ethernet, WIFI etc / - Internet – control movement of packets / - Transport – data connection / - Application – User interaction , email / - Physical – Cables, NIC / - Datalink – Ethernet, Switches / - Network – IP, Routers / - Transport – TCP, UDP / - Application – HTTP, FTP, SMTP
	Switch	Connects devices within the same network. / LAN network. / Forwards data packets to and from those devices. / Only sends the data to the devices it is inteded for.
	Router	Connects two or more subnetworks. / 1) Manage traffic between these two networks by forwarding data packets to their intended IP address. / 2) Allow multiple devices to use the same internet connection.
	Router work	1) Direct and guide the packets that are sent so they get to their IP address. / 2) Uses internal routing table. List of paths to various network destination. / 3) Reads the packet header to know where it is heading to, Consult the table to decide which path is most efficient.
	Modem vs Router	1) Modem connect one device (example a router or a PC) to the Internet. / 2) Router makes a LAN connection between devices, but no access to the Internet. / 3) Connect Router to Modem to provide Internet connection to all devices on LAN.
	Loopback address	Built into the IP domain system in order for a device to send and receive its own data packets. / 127.0.0.0 to 127.255.255.255 / Used for various kind of analysis, for testing purposes and debugging.
	Subnet	A network inside a network. / Divide large network into smaller ones. / Use part of HOST IP address. / NETWORK SUBNET HOST fields. / IP address to identify the subnet. / Another one to identify the broadcast subnet address. / Network traffic travel shorter distance.
	Calculate subNet mask from IP addr	1. Find Subnet number / 2. Find Subnet size / 3. Find Broadcast address / 4. Locate IP address Subnet / 5. Calculate Valid hosts / Subnet Address / Min Host Address / Max Host Address / Broadcast Address
	Network and Host part of IP Address	1s in subnet mask that cross out with IP address is Network Address / 0s in subnet mask that cross out with IP address is Host Address
	Broadcast	Broadcast do not go past Router, they remain within Network.

### Important Concepts:

- TCP – used to send packet over the internet. Transmission Control Protocol.
- IP Address: Network Layer
IP addressing – assign addresses to devices on a network. Aunique IP address.
- Identify HOST (such as computer ) / HOST is a NETWORK INTERFACE?
- Identify NETWORK it belongs to.
TCP/ IP uses SUBNET MASK to separate the two.

CIDR and SUBNET MASK are both used to define the range of IP addresses available within a network, but they serve slightly different purposes.

Public IP Address – assigned to your network router by your Internet service provider.
- helps to connect to the internet from inside your network, to outside your network
Private IP Address – assigned to your device by your network router
When a network is connected to the internet, it cannot use an IP address from the reserved private IP addresses.

Find Network address of IP address:
IP address | 01101000.11000110.11110001.01111101
Mask | 11111111.11111111.11111111.10000000
do bitwise AND
Network address | 01101000.11000110.11110001.00000000

104.198.241.0
Use online tools - IP to Binary converter and Binary to IP converter / Binary to Decimal converter

Find the Range of Host address:

IP address | 01101000.11000110.11110001.01111101
Mask | 11111111.11111111.11111111.10000000
The range is taken from the last 7 bits of the mask, which is all 0.
Therefore the range is 000 000 0 - 111 111 1
0 – 127
The extremities of the range are reserved as
1. NETWROK ADDRESS:	0	→ 104.198.241.0
2. BROADCAST ADDRESS: 127	→ 104.198.241.127
Therefore the real IP RANGE is : 104.198.241.1 – 104.198.241.126
All hosts on a subnetwork have the same network prefix, unlike the host identifier, which is a unique local identification.

#### CIDR Notation.
CIDR /24 means the subnet mask is 255.255.255.0?
CIDR /24 means it allows 24 bits of network, and 8 bits of host address.
Therefore 2^8 =
Example: CIDR /25
IP address | 01101000.11000110.11110001.01111101
Mask | 11111111.11111111.11111111.10000000
Equivalent to a mask of /25
Note,there are 25 bits of the Mask representing the NETWORK ADDRESS.
- Ports act as interfaces on Routers and Switch through which the physical LAN cable is connected.
- In Routers Ports act as both Connectivity interface and Routing interface.
- The router’s software configuration determines whether a particular port function as a routing interface or simply as a connectivity interface within LAN.
- In Switch Ports act as Connectivity interface.

Switch:
There is no routing interface.
Do they have IP Address? Yes, if they are Managed switches, to allow for remote	configuration, monitoring and management.
But if they are Unmanaged Switches, they do not have IP addresses and operate at the data	link layer (Layer 2) of the OSI model, primarily forwarding Ethernet frames based on MAC	addresses.
Router:
- Connects multiple devices on a single network
- Connects multiple networks together
- has an interface for each network it connects to
Since the ROUTER separates different networks, the range of possible IP addresses on one interface must NOT overlap with the range of its other interfaces.
An overlap in the IP address range would imply that the interfaces are on the same Network.

Understanding IP ADDRESSES associated with ROUTER:
- Routers can have multiple network addresses (corresponding to their interfaces). Each network segment they are connected to is facilitated by an interface, and this can be LANs or VLANs.
- And they also have their own IP address for management and administrative purposes.
ROUTING TABLE:
A routing table is a data table stored in a router or a network host (Computer, Laptop, Servers, Printers).
DESTINATION:	Network Address on which the target HOST is situated.
NEXT HOP:	Next closest ROUTER enroute to target HOST.
Destination field set to Default.
The route of default or 0.0.0.0/0, is the route that takes effect when no other route is available for an IP destination address.
The default route will use the next-hop address to send the packets on their way without giving a specific destination.
The default route will match any network.
## This table assumes you are starting with a /24 network and then subnetting it into smaller subnets as indicated by each CIDR notation.
CIDR Notation	Number of Subnets	Number of IP Addresses per Subnet	Number of Usable IP Addresses per Subnet
/24	1	256	254
/25	2	128	126
/26	4	64	62
/27	8	32	30
/28	16	16	14
/29	32	8	6
/30	64	4	2
/31	128	2	0*
/32	256	1	0*

In each subnet, the first IP address is the network address and the last IP address is the broadcast address, so they are not usable for hosts.
/31 is typically used for point-to-point links where there are exactly two devices, so while technically it has no usable host addresses, both IPs are usable for communication.
/32 specifies a single IP address, usually used for host routes or specific device addresses, so there are no additional usable IP addresses.
# Reserved private IP ranges (Standardized):
192.168.0.0 - 192.168.255.255 (65,536 IP addresses)
172.16.0.0 - 172.31.255.255 (1,048,576 IP addresses)
10.0.0.0 - 10.255.255.255 (16,777,216 IP addresses)
127.0.0.0 – 127.255.255.255
# Given IP address 191.75.240.64 Subnet mask 255.255.255.0
Subnet number:	191.75.240.0	(a.k.a Network ID)
Subnet size:	256 addresses
Broadcast address:	191.75.240.255
IP address subnet:	191.75.240.0/24
Valid hosts:	254
Minimum host address:	191.75.240.1
Maximum host address:	191.75.240.254

What is the IP-range AND number of subnets for CIDR/ 18
- 63.239.0.0 - 63.239.63.255
- 63.239.64.0 - 63.239.127.255	←
- 63.239.128.0 - 63.239.191.255
- 63.239.192.0 - 63.239.255.255
- Therefore if your Private IP addresses are 63.239.100.52 AND 63.239.100.53
- Pay attention to the 3rd Octet, because CIDR/18 concerns 3rd Octet.
- Our fixed IP is part of 63.239.64.0 – 63.239.127.255 range. ←
- So the network-address is 63.239.64.0, combine this with our mask of /18
- Tihis is the destination of our routing table, 63.239.64.0/18.

Level 10 QUESTION:
How to resolve overlap issue?
The trick is in identifying the range that is available between 0 and 255.
CHAT GPT: https://chatgpt.com/share/21280c97-4c03-49bb-be6b-8a61d5a02776
It comes down to this:
Interface 11
136.108.183.0/25:	136.108.183.0 – 136.108.183.127
Interface 23
136.108.183.128/26:	136.108.183.128 - 136.108.183.191
Interface 13
136.108.183.252/30:	136.108.183.252 - 136.108.183.255

What is the available range for interface R22?
Notice above between 192 and 251 is not taken.
So I must go for network ID that begins 192.

on CIDR/30
136.108.183.192/30:	136.108.183.192 – 136.108.183.195
on CIDR/29
136.108.183.192/29:	136.108.183.192 – 136.108.183.199
on CIDR/28
136.108.183.192/28:	136.108.183.192 – 136.108.183.207
on CIDR/27
136.108.183.192/28:	136.108.183.192 – 136.108.183.223

but I can’t use CIDR/26, because it overlaps
136.108.183.192/28:	136.108.183.192 – 136.108.183.255

Connectivity between 2 ROUTERS.
Interfaces connecting two routers must be on the same subnet to communicate directly.
There is no requirement for logical ordering of IP ranges between subnets, as long as there is no overlap between any of the subnets.